PICO B21
2017.4.1.
V1.0

---
PCBA Function Block
+12VDC Input
i.MX6 Dual
Processor
1GHz
1x Lockable
DC Power Jack
1/2GB DDR3
Memory
DDR3-1066
1x HDMI Type-A
Connector
1x LVDS
Connector
HDMI / I2C2
18/24-bit, 2-ch LVDS
1x RJ45 Ethernet
Connector
KSZ9031RNX
GbE Controller
I2S
SGTL5000
Audio Codec
Line-out
1x Line-out
Wafer
GbE
RGMII
I2C3
MIC-in
1x RJ45 Ethernet
Connector
LAN9500A
10/100 Controller
Audio-out
1x Mic-in
Wafer
10/100
2x USB2.0 Type-A
Connectors
IS31AP2010B
3W Audio Amplifier
2x SPKR-out
Wafer
USB7
SPKR-out
USB1/2
1x USB2.0
Wafer
USB2517
USB2.0 Hub
1x Micro-USB
Connector
USB OTG
USB Host
USB3
1x Micro-SD
Card Cage
SD3
USB6
1x mPCIE
Socket
4/8GB eMMC
NAND Flash
PCIE
SD4
I2C3
RS232/422/485
Transceiver
1x COM1
Wafer
SIM
UART1
RS232
/422
/485
1x Micro-SIM
Card Holder
RS232/422/485
Transceiver
1x COM2
Wafer
UART5
GPIO
RS232
/422
/485
Discrete
Power
MMPF0100F0AEP
PMIC
Power Rail
1x GPIO
Wafer
Power Rail
GPIO / SPI / I2C1
I2C2
1x FP
Header
PWR_EN
PWR / Reset Switch
Reset
1x MCU Update
Header
EFM32TG110F16
MCU
1x Debug
Header
I2C3
JTAG
UART2

---
PCBA Connectors (1/13)
BAT1	CR2032
SW1	Boot Configuration Select
JP4	Back Light Enable Select
JP5	LVDS Power Voltage Select
CN1	Microphone
CN2	Headphone
CN3	Left Speaker
CN4	Right Speaker
CN5	COM1
CN6	COM2
CN7	GPIO /SPI /I2C
CN8	USB OTG
CN9	HDMI
CN10	FRONT PANEL
CN12	USB Port
CN13	MCU Update Test Point
CN14	Ethernet Gigabyte
CN15	Ethernet
CN16	USB Port
CN17	Power Jack
CN20	CAN Port

---
PCBA Connectors (2/13)
CN11	Debug PORT
CN18	LED Driver Connector
CN19	Micro SD CARD Socket
SIM1	SIM CARD Socket
MPCIE1	Mini-PCI
LVDS1	LVDS Connector

---
PCBA Connectors (3/13)
SW1
SW1
4	3	2	1
x	0	0	0	Ext. SD Boot
x	1	1	1	eMMC Boot
4
3
2
1
ON
1
2
+3V
GND
BAT1

---
PCBA Connectors (4/13)
JP4
1-3	2-4	BL_EN 恆為 3.3V
	4-6	BL_EN 由 CPU 控制，0V/3.3V
3-5	2-4	BL_EN 恆為 5V
	4-6	BL_EN 由 CPU 控制，0V/5V
JP5
Back light	1-3	Back light VDD為 12V
	3-5	Back light VDD 為 5V
LVDS Power	2-4	LVDS VDD 為 3.3V
	4-6	LVDS VDD 為 5V
JP4
1
3
5
2
4
6
3.3V
5V
LVDS1_BLT_CTRL
BL_EN
JP5
1
3
5
2
4
6
12V
5V
5V
3.3V

---
PCBA Connectors (5/13)
LOUT_R
LOUT_L
GND
SENSE (Micro phone detect)
LOUT_R
LOUT_L
GND
SENSE (Head phone detect)
CN1 (MIC)
1
2
3
4
CN2 (Headphone)
1
2
3
4
Speaker +
Speaker -
CN3
1
2
Speaker +
Speaker -
CN4
1
2

---
PCBA Connectors (6/13)
RS232
RS485
RS422
DCD (R1)
D+
TXD+
RXD (R2)
RX(I)
D-
TXD-
RTS (R7)
RTS(O)
TXD (R3)
TX(O)
RXD+
CTS(I)
CTS (R8)
RXD-
DTR (R4)
GND
VCC_5V
CN5
1
2
3
4
5
6
7
8
9
10

---
PCBA Connectors (7/13)
RS232
RS485
RS422
RS232 Full Function
DCD (R1)
DCD
D+
TXD+
DSR (R6)
DSR
RXD (R2)
RXD
RX(I)
D-
TXD-
RTS (R7)
RTS
RTS(O)
TXD (R3)
TXD
TX(O)
RXD+
CTS
CTS(I)
CTS (R8)
RXD-
DTR (R4)
DTR
RI (R9)
RI
GND
VCC_5V
RS232 Full Function
1. 當要使用時，模式會固定為 RS232
2. 需上件 0 歐姆電阻 R363 , R364 , R358 , R359 , R360
3. 需移除 R354 , R355 的 0 歐姆電阻
CN6
1
2
3
4
5
6
7
8
9
10

---
PCBA Connectors (8/13)
CN7
1
2
3
4
5
6
7
8
9
10
VCC_5V
GPIO1
GPIO2
SPI_CLK
SPI_MOSI
SPI_MIOS
SPI_SS0
I2C1_SCL
I2C1_SDA
GND
CN8
1
2
3
4
5
VBUS
D-
D+
ID
GND

---
PCBA Connectors (9/13)
1
3
5
7
9
11
13
15
17
19
2
4
6
8
10
12
14
16
18
CN9
TMD Data2+
TMD Data2-
GND
GND
TMD Data1+
TMD Data1-
TMD Data0+
TMD Data0-
GND
TMD Clock+
TMD Clock-
GND
GND
CEC
DDC_CLK
HPDET
DDC DATA
+5V
CN10
1
3
5
2
4
6
PWRBTN
nRESET
3.3V
GND
7
8
GND
GND
3.3V
LED_WWAN
CN11
1
2
3
4
3.3V
RX
TX
GND

---
PCBA Connectors (10/13)
VCC
D-
CN12
1
2
3
4
D+
GND
CN13
1
2
3
4
5
VMCU
RESETn
SWDIO
SWCLK
GND
CN14
1
2
3
4
5
6
7
8
TxRx A+ DC+
TxRx A- DC+
TxRx B+ DC-
TxRx C+
TxRx C-
TxRx B- DC-
TxRx D+
TxRx D-
CN15
1
2
3
4
5
6
7
8
TxRx A+ DC+
TxRx A- DC+
TxRx B+ DC-
TxRx C+
TxRx C-
TxRx B- DC-
TxRx D+
TxRx D-

---
PCBA Connectors (11/13)
CN17
Bottom
Top
DC-IN 12V
1
2
DC-IN GND
1
2
CANH
CANL
CN20
3
GND
BL_PWM
CN18
1
2
3
4
GND
BL_VDD
5
6
7
BL_VDD
GND
BL_EN
CN16
1
2
3
4
1
2
3
4
VCC
D-
D+
GND
VCC
D-
D+
GND
A
B
CN19
8
7
6
5
4
3
2
1
DAT2
DAT3
CMD
VDD
CLK
GND
DAT0
DAT1

---
PCBA Connectors (12/13)
LVDS1 (1/2)
LVDS1 (2/2)
16
B1+
(LVDS1_TX1_P)
17
GND
18
B2-
(LVDS1_TX2_N)
1
A0-
(LVDS0_TX0_N)
19
B2+
(LVDS1_TX2_P)
2
A0+
(LVDS0_TX0_P)
20
BCK-
(LVDS1_CLK_N)
3
A1-
(LVDS0_TX1_N)
21
BCK+
(LVDS1_CLK_P)
4
A1+
(LVDS0_TX1_P)
22
B3-
(LVDS1_TX3_N)
5
A2-
(LVDS0_TX2_N)
23
B3+
(LVDS1_TX3_P)
6
A2+
(LVDS0_TX2_P)
24
GND
7
GND
25
8
ACK-
(LVDS0_CLK_N)
26
9
ACK+
(LVDS0_CLK_P)
27
10
A3-
(LVDS0_TX3_N)
28
VDD
11
A3+
(LVDS0_TX3_P)
29
VDD
12
B0-
(LVDS1_TX0_N)
30
VDD
13
B0+
(LVDS1_TX0_P)
14
GND
15
B1-
(LVDS1_TX1_N)

---
PCBA Connectors (13/13)
MPCIE1
1
3
5
7
9
11
13
15
2
4
6
8
10
12
14
16
17
19
21
23
25
27
29
31
18
20
22
24
26
28
30
32
34
36
38
40
42
44
46
48
50
52
33
35
37
39
41
43
45
47
49
51
WAKE#
Reserved
Reserved
Reserved
GND
REFCLK-
REFCLK+
GND
Reserved
Reserved
GND
PERn0
PERp0
GND
GND
PETn0
PETp0
GND
GND
3.3V
3.3V
GND
Reserved
Reserved
Reserved
Reserved
3.3V
GND
1.5V
UIM_PWR
UIM_DATA
UIM_CLK
UIM_RESET
UIM_VPP
GND
W_DISABLE#
PERST#
3.3V
GND
1.5V
SMB_CLK
SMB_DATA
GND
USB_D-
USB_D+
GND
KED_WWAN#
Reserved
Reserved
1.5V
GND
3.3V
SIM1
2
4
6
5
3
1
UIM_PWR
UIM_RESET
UIM_CLK
GND
UIM_VPP
UIM_DATA

---
客戶需求
- 提供 EFM-MCU 電源控制
  - DC IN 即供電
  - WDOG = 10 sec, Retry 3 Times
  - Button switch = 1 sec
- 提供PICO-B21相關組態的BSP
  - MX60T (DDR3 1G Bytes, EMMC 4GB)
  - MX61T (DDR3 2G Bytes, EMMC 4GB)
  - MX62T (DDR3 1G Bytes, EMMC 8GB)
  - MX63T (DDR3 2G Bytes, EMMC 8GB)
- 硬體IO驗證
- 提供HW測試程式 – PCBA function Test
  - PCBA	單一測試
  - RT	可靠性測試
  - Boot Test	開關機測試
  - Stress Test	重載測試
- 提供廠端MP 測試程式
  - 手動判斷測試
  - 自動判斷測試
  - 序號 及 MAC輸入
- 提供Chamber Test
  - 取消Uboot及Kernel 溫度相關保護
- 提供ESD & EMI Test
  - 針對case輸出IO提供測試
  - UART1, UART5, LAN0, LAN1
  - HDMI, Headphone, USB

---
時程
2017/5/14 Project Start
2017/6/7 IO驗證完成,提供
 PCBA function Test, MCU firmware
2017/6/14提供Chamber 及 ESD & EMI 測試程式
2017/6/13 MP Release, 提供所有組態BSP
2017/6/02 拿到PICO-B21
提供 EFM-MCU 電源控制
- 提供PICO-B21相關組態的BSP
- 硬體IO驗證
- 提供HW測試程式 – PCBA function Test
- 提供廠端MP 測試程式
- 提供Chamber Test
- 提供 ESD & EMI Test
3 月
4 月
5 月
6 月
7 月
8 月
9 月
已完成
未完成
取消

---
提供 EFM-MCU 電源控制
- DC IN直接供電
- 提供PWRBTN功能
- 提供WDOG功能
- Retry Times三次
- RTC功能
- 電源時序控制
- PMIC電壓偵測
- LED 控制

---
硬體IO驗證
- Ethernet
  - 確認可否PING 8.8.8.8
- USB
  - 確認可否Read/Write
- HDMI
  - 確認影像是否有輸出
- LVDS
  - 確認影像是否有輸出
- UART
  - 確認RS232/ RS485/ RS422功能正常
- GPIO
  - 確認可否正常控制
- SPEAKER
  - 確認聲音正常輸出
- Headphone
  - 確認聲音正常輸出
  - 插入及SPEAKER靜音
- Microphone
  - 確認可否錄音
- CAN
  - 確認通訊正常

---
PCBA function測試
- 請執行PCBA_TEST
- 文件 PFT/readme.pdf
- 搭配PCBA測試治具
  - 網路線
  - USB隨身碟
  - HDMI (Cable + Panel)
  - 喇叭
  - 耳機
  - 麥克風
  - LVDS
  - UART1/ UART5
  - GPIO/ I2C/ SPI
  - CAN

---
MP 測試
- MP 測試治具
- 文件mp-tools/readme.pdf
- 執行mp-tools.py
  - 手動測試項目
  - 自動測試項目
  - 輸入序號
  - 輸入Mac Address
  - 輸出測試結果

---
EMI & ESD 測試
- 針對鐵殼外露部份
  - Com Port
  - USB Port
  - LAN Port
  - HDMI Port
  - Headphone
  - Keyboard & Mouse
- 執行main.sh
  - 確認測試過程,IO Function 仍然正常

---
Chamber測試
- uboot 開機溫度限制變更
- Kernel 相關溫度限制移除
- 提供Ubuntu BSP, 使在溫箱測試中時, 瞭解在軟體無保護情況下板端的狀況